## Slide 1: Dynamic Control of Software-Defined Networks
Xin Jin
Committee: Jennifer Rexford (advisor),
David Walker, Ratul Mahajan, Nick Feamster, Aarti Gupta

## Slide 2: Traditional network
Network
Control
Control
Control
Control
Control
Coupled data plane (switch hardware) and control plane (switch software)
Closed, proprietary interface
Hard to change and innovate

## Slide 3: Software-Defined Networking (SDN)
Decoupled data plane and control plane
Open interface, e.g., OpenFlow
Easy to change and innovate
Network
Control Platform
Control Plane
Data Plane
Network Services

## Slide 4: This talk:
New algorithms and systems
to build the network control platform

## Slide 5: Challenge 1: Many services
Routing
Load
Balancing
Monitoring
Firewall
Control Platform
Network
Services
Composing multiple services
Defending against malicious and buggy services
Providing flexibility in choosing programming languages for development

## Slide 6: Challenge 2: Many events
E
A
D
B
C
Network
Traffic shift
Host mobility
Cyber attack
Device failure
Server overload
Device upgrade

## Slide 7: Challenge 2: Many events
Traffic shift
Congestion
Revenue loss
100 ms slowdown reduces sales by 1%
100 ms slowdown reduces # searches by 0.2%
400 ms slowdown reduces traffic by 9%
http://www.gduchamp.com/media/StanfordDataMining.2006-11-28.pdf
http://services.google.com/fh/files/blogs/google_delayexp.pdf
http://www.slideshare.net/stoyan/yslow-20-presentation/4-The_importance_of_performance_ulli500

## Slide 8: Challenge 2: Many events
Composing updates from multiple applications
Distributing updates across multiple switches

## Slide 9: Challenge 3: Many layers
Network Layer
Optical Layer
Network switch (Router)
Optical switch

## Slide 10: Challenge 3: Many layers
Jointly managing the network and optical layers
Dynamically changing device configurations in face of network events
Coordinating updates between the network and optical layers

## Slide 11: Contributions
Efficient
algorithm
System
prototype
CoVisor
[NSDI’15]
Efficient policy compilation
Open-source prototype, integrated into ONOS
Dionysus
[SIGCOMM’14]
Efficient update scheduling
Prototype on real testbed, evaluation on realistic data
Owan
[SIGCOMM’16]
Efficient topology reconfiguration
Prototype on real testbed, evaluation on realistic data

## Slide 12: CoVisor: Dynamic Service Composition
[NSDI’15] Xin Jin, Jennifer Gossels, Jennifer Rexford, David Walker, “CoVisor: A compositional hypervisor for software-defined networks”, in USENIX Symposium on Networked Systems Design and Implementation (NSDI), May 2015.

## Slide 13: Goal: Manage multiple services on the same network
Routing
Load
Balancing
Monitoring
Firewall
Control Platform
Network

## Slide 14: Operation of network services
E
A
D
B
C
Routing
1
2
3
Priority | Match | Action
1 | dstip=2.0.*.* | fwd(2)
0 | * | fwd(3)
Network
Policy on switch A
“other traffic”
dstip=2.0.*.*

## Slide 15: What if we have more than one service?

## Slide 16: Example: Composing two policies
1
2
3
Priority | Match | Action
7 | dstip=2.0.0.0 | fwd(2)
0 | * | fwd(3)
Priority | Match | Action
3 | srcip=1.0.0.* | count
0 | * | count
Monitoring on srcip
Routing on dstip
Problem: How to combine two policy tables into a single policy table to be installed on the switch?
Switch

## Slide 17: Simply installing two policy tables on the switch does not work
Priority | Match | Action
3 | srcip=1.0.0.* | count
0 | * | count
7 | dstip=2.0.0.0 | fwd(2)
0 | * | fwd(3)
What if we have a packet with srcip=1.0.0.0 and dstip=2.0.0.0? Only forwarded, not counted!
Priority | Match | Action
7 | dstip=2.0.0.0 | fwd(2)
0 | * | fwd(3)
Priority | Match | Action
3 | srcip=1.0.0.* | count
0 | * | count
Monitoring on srcip
Routing on dstip

## Slide 18: Overview of service management
Well-defined composition interface and semantics
  Parallel composition (||)
  Sequential composition (>>)
  Override composition ( )
Network operator: use the interface to specify the relationship between multiple services
CoVisor: use efficient algorithms to compile multiple policy tables into a single policy table

## Slide 19: Parallel composition (||) [ICFP’11]
Two services process packets in parallel
Computing a cross-product for the composition
Priority | Match | Action
7 | dstip=2.0.0.0 | fwd(2)
0 | * | fwd(3)
Priority | Match | Action
3 | srcip=1.0.0.* | count
0 | * | count
Priority | Match | Action
? | srcip=1.0.0.*, dstip=2.0.0.0 | count, fwd(2)
? | srcip=1.0.0.* | count, fwd(3)
? | dstip=2.0.0.0 | count, fwd(2)
? | * | count, fwd(3)
Monitoring
Routing
A packet with srcip=1.0.0.0 and dstip=2.0.0.0 is both counted and forwarded.

## Slide 20: Key challenge: Efficiently handle policy updates
Computation overhead
  The computation time to compile policy updates
Rule-update overhead
  The rule-updates to update switches to the new policy
Priority | Match | Action
7 | dstip=2.0.0.0 | fwd(2)
5 | dstip=2.0.0.* | fwd(1)
0 | * | fwd(3)
Priority | Match | Action
? | srcip=1.0.0.*, dstip=2.0.0.0 | count, fwd(2)
? | srcip=1.0.0.* | count, fwd(3)
? | dstip=2.0.0.0 | count, fwd(2)
? | * | count, fwd(3)
Routing
Priority | Match | Action
3 | srcip=1.0.0.* | count
0 | * | count
Monitoring

## Slide 21: Naïve solution
Priority assignment: linearly increase from bottom
Update overhead
  m, n: sizes of two policies in composition
  Computational overhead: O(mn)
  Rule-update overhead: O(mn)
Priority | Match | Action
3 | ∙∙∙ | ∙∙∙
2 | ∙∙∙ | ∙∙∙
1 | ∙∙∙ | ∙∙∙
0 | ∙∙∙ | ∙∙∙
Update
Priority | Match | Action
5 (3) | ∙∙∙ | ∙∙∙
4 (new) | ∙∙∙ | ∙∙∙
3 (2) | ∙∙∙ | ∙∙∙
2 (1) | ∙∙∙ | ∙∙∙
1 (new) | ∙∙∙ | ∙∙∙
0 (0) | ∙∙∙ | ∙∙∙

## Slide 22: Incremental update
Priority assignment: add priorities of original policies
Update overhead
  m, n: sizes of two policies in composition
  Computational overhead: O(m+n)
  Rule-update overhead: O(m+n)
Priority | Match | Action
3+7=10 | ∙∙∙ | ∙∙∙
3+0=3 | ∙∙∙ | ∙∙∙
0+7=7 | ∙∙∙ | ∙∙∙
0+0=0 | ∙∙∙ | ∙∙∙
Update
Priority | Match | Action
3+7=10 | ∙∙∙ | ∙∙∙
3+5=8 (new) | ∙∙∙ | ∙∙∙
3+0=3 | ∙∙∙ | ∙∙∙
0+7=7 | ∙∙∙ | ∙∙∙
0+5=5 (new) | ∙∙∙ | ∙∙∙
0+0=0 | ∙∙∙ | ∙∙∙

## Slide 23: Sequential composition (>>) [NSDI’13]
Two services process packets one after another
Priority assignment: concatenate priorities
Pri. | Match | Action
1 | dstip=10.0.0.1 | fwd(1)
∙∙∙ | ∙∙∙ | ∙∙∙
Pri. | Match | Action
3 | srcip=0.0.0.*, dstip=1.2.3.4 | dstip=10.0.0.1
∙∙∙ | ∙∙∙ | ∙∙∙
Priority | Match | Action
 | srcip=0.0.0.*, dstip=1.2.3.4 | dstip=10.0.0.1, fwd(1)
3 ◦ 1 = 25
011
001
High
Bits
Low
Bits
Load balancing: Choose server, rewrite dstip
Routing: Route based on dstip

## Slide 24: Override composition ( ) [CoVisor’15]
One service chooses to act or defer the processing to another service
Priority assignment: offset priorities
Priority | Match | Action
1 | dstip=2.0.*.* | fwd(2)
0 | * | fwd(3)
Priority | Match | Action
1 + 8 (max priority of D) = 9 | srcip=1.0.0.0, dstip=2.0.0.0 | fwd(1)
1 | dstip=2.0.*.* | fwd(2)
0 | * | fwd(3)
Pri. | Match | Action
1 | srcip=1.0.0.0, dstip=2.0.0.0 | fwd(1)
Elephant Flow Routing (E)
Default Routing (D)

## Slide 25: Topology management
Abstraction: Each service operates on a virtual topology
Benefits: Information hiding, portability, composition, etc.
Network OS
Service
Service
Service
Challenge: Devirtualization
  Compile policies from the virtual network to the physical network
Devirtualization algorithm
  Symbolic analysis + sequential composition

## Slide 26: Access control
Abstraction: Each service operates on a virtual switch model
Benefits: Defend against malicious or buggy services
Virtual switch model: Limited functionalities
  Constraint on visibility: What header fields can match, e.g., IP routing cannot see MAC addresses , TCP/UDP ports
  Constraint on capability: What actions can perform, e.g., IP routing cannot modify any packet header fields

## Slide 27: Implementation and Evaluation
Implementation
  Open-source prototype: https://github.com/xinjin/CoVisor
  Integrated into ONOS with
Evaluation
  Sequential composition: L3-L4 Firewall >> L3 Router
  Parallel composition: L2 Monitor || L2 Router
  Topology virtualization: Gateway between an Ethernet island and an IP core

## Slide 28: Evaluation: L3-L4 Firewall >> L3 Router
  Computation overhead of inserting one rule to L3-L4 Firewall Policy
Chart: L3 Router Policy Size (Log-Scale)
| 1k | 2k | 4k | 8k | 16k | 32k
Naïve | 20.2981 | 41.0695 | 85.1378 | 207.366 | 653.771 | 1295.2058
Incremental | 0.23764 | 0.55557 | 1.1021 | 3.0395 | 6.9085 | 13.2903

## Slide 29: Evaluation: L3-L4 Firewall >> L3 Router
Chart: L3 Router Policy Size (Log-Scale)
| 1k | 2k | 4k | 8k | 16k | 32k
Naïve | 10293.19 | 19538.98 | 37984.67 | 74979.24 | 184927.41 | 368753.53
Incremental | 138.74 | 275.79 | 549.98 | 1101.25 | 2202.71 | 4401.5
  Rule-update overhead of inserting one rule to L3-L4 Firewall Policy

## Slide 30: Summary: CoVisor is a network hypervisor for service compositions
1
Efficient algorithm
Incrementally compile policy compositions and updates
2
System prototype
Project website: http://covisor.cs.princeton.edu
Integrated into ONOS with

## Slide 31: Dionysus: Dynamic Update Scheduling
[SIGCOMM’14] Xin Jin, Hongqiang Harry Liu, Rohan Gandhi, Srikanth Kandula, Ratul Mahajan, Ming Zhang, Jennifer Rexford, Roger Wattenhofer, “Dynamic scheduling of network updates”, in ACM SIGCOMM, August 2014.

## Slide 32: What is network update
Control Platform
E
A
D
B
C
Network
Updating policy tables in switches

## Slide 33: Example of network update
Current State
A
D
C
B
E
F4: 5
F2: 5
F3: 10
Target State
F1: 5
F4: 5
F2: 5
F3: 10
A
D
C
B
E
Update
F1: 5
Flow ID
Flow Size
Link capacity: 10 units

## Slide 34: Goals for network update
1
Time: Fast response to dynamics
Quick adaptation to failures, host mobility, cyber attacks, etc.
2
Consistency: Smooth transient behavior
Loop, blackhole, access control violation
Congestion

## Slide 35: What is consistent network update
Asynchronous updates can cause congestion
Need to carefully order update operations
Current State
A
D
C
B
E
F1: 5
F4: 5
F2: 5
F3: 10
Target State
F1: 5
F4: 5
F2: 5
F3: 10
A
D
C
B
E
Transient State
A
D
C
B
E
F1: 5
F4: 5
F2: 5
F3: 10
Congestion on B-E

## Slide 36: Existing solutions are slow
Existing solutions are static [ConsistentUpdate’12, SWAN’13, zUpdate’13]
  Pre-compute an order for update operations
Downside: Do not adapt to runtime conditions
  Slow in face of highly variable operation completion time
  Measurement: >10X difference between the median and the 99th percentile for operation completion time
F3
F4
F2
F1
Static
Plan A
F3
F4
F2
F1
Static
Plan B

## Slide 37: Static schedules can be slow
F3
F4
F2
F1
Static
Plan B
F3
F4
F2
F1
Static
Plan A
F1
F2
F3
F4
Time
1
2
3
4
5
F1
F2
F3
F4
Time
1
2
3
4
5
F1
F2
F3
F4
Time
1
2
3
4
5
F1
F2
F3
F4
Time
1
2
3
4
5
Current State
A
D
C
B
E
F1: 5
F4: 5
F2: 5
F3: 10
Target State
F1: 5
F4: 5
F2: 5
F3: 10
A
D
C
B
E
Update
No static schedule is a clear winner under all conditions!

## Slide 38: Dynamic schedules are adaptive and fast
F3
F4
F2
F1
Static
Plan B
F3
F4
F2
F1
Static
Plan A
Current State
A
D
C
B
E
F1: 5
F4: 5
F2: 5
F3: 10
Target State
F1: 5
F4: 5
F2: 5
F3: 10
A
D
C
B
E
Update
No static schedule is a clear winner under all conditions!
F3
F4
F2
F1
Dynamic
Plan
Adapts to actual conditions!

## Slide 39: Challenges of the scheduling problem for network updates
1
Multiple resources
Updating a flow affects multiple links (link capacity resource) and switches (switch rule table resource)
2
Resource consumption and release
Updating a flow consumes resources on new paths and releases resources on old paths

## Slide 40: Idea: Use a dependency graph to represent a network update
Operation node: Represent flow update operations
Resource node: Represent resources, i.e., link capacity and switch table size
Node
Edge
Represent resource consumption and release between operation nodes and resource nodes

## Slide 41: Example for dependency graph
Current State
A
D
C
B
E
F1: 5
F4: 5
F2: 5
F3: 10
Target State
F1: 5
F4: 5
F2: 5
F3: 10
A
D
C
B
E
Update
Move
F3
Move
F1
Move
F2
B-E: 0
A-E: 0
Move
F4
No free capacity
on B-E

## Slide 42: Example for dependency graph
Current State
A
D
C
B
E
F1: 5
F4: 5
F2: 5
F3: 10
Target State
F1: 5
F4: 5
F2: 5
F3: 10
A
D
C
B
E
Update
Move
F3
Move
F1
Move
F2
B-E: 0
A-E: 0
Move
F4
5
5
Moving F2
requires 5 units
of capacity on B-E
Moving F2
releases 5 units
of capacity to A-E

## Slide 43: Example for dependency graph
Current State
A
D
C
B
E
F1: 5
F4: 5
F2: 5
F3: 10
Target State
F1: 5
F4: 5
F2: 5
F3: 10
A
D
C
B
E
Update
Move
F3
Move
F1
Move
F2
B-E: 0
A-E: 0
Move
F4
10
5
5
5
5

## Slide 44: Example for dependency graph
Current State
A
D
C
B
E
F1: 5
F4: 5
F2: 5
F3: 10
Target State
F1: 5
F4: 5
F2: 5
F3: 10
A
D
C
B
E
Update
Move
F1
Move
F2
B-E: 10
A-E: 0
Move
F4
5
5
5
5

## Slide 45: Adaptive critical-path scheduling
Schedule operation nodes on critical paths first
Update dependency graph when operations finish
Recompute critical paths on updated dependency graph
Critical path

## Slide 46: Handling cycles
A-B: 0
Move
F2
Move
F1
C-D: 0
A-B: 5
Move
F3
Move
F4
5
20
5
5
20
20
20

## Slide 47: Handling cycles
A-B: 0
Move
F2
Move
F1
C-D: 0
A-B: 5
Move
F3
Move
F4
5
20
5
5
20
20
20
Schedule

## Slide 48: Handling cycles
Move
F2
Move
F1
C-D: 0
A-B: 0
20
20
20
20
Deadlock!

## Slide 49: Handling cycles
A-B: 0
Move
F2
Move
F1
C-D: 0
A-B: 5
Move
F3
Move
F4
5
20
5
5
20
20
20
Partial
movement

## Slide 50: Handling cycles
A-B: 0
Move
F2
Move
F1
C-D: 5
A-B: 0
Move
F3
Move
F4
5
15
5
5
15
20
20
Partial movement for 4 rounds
to resolve the cycle

## Slide 51: Network update pipeline
Dependency Graph Generator
Update Scheduler
Network
Current
State
Target
State
Consistency
Property

## Slide 52: Implementation and evaluation
Implementation
  Software: Controller prototype
  Hardware: Testbed with 8 Arista switches that emulates a wide area network
Evaluation: traces and topologies from a cloud service provider
  Wide area network (WAN): ~50 sites
  Data center network (DC): ~500 switches

## Slide 53: Evaluation: Update time for traffic engineering updates
Chart: Media Update Time (second)
| WAN TE | Data Center TE
SWAN | 1.496 | 3.297
Our solution | 0.795 | 1.819
(State-of-the-Art)

## Slide 54: Summary: Dionysus is a scheduler for fast and consistent network updates
1
Efficient algorithm
Dynamically schedule update operations
2
System prototype
Prototype on real testbed, evaluation on topology and traces from Microsoft networks

## Slide 55: Owan: Dynamic Topology Reconfiguration
[SIGCOMM’16] Xin Jin, Yiran Li, Da Wei, Siming Li, Jie Gao, Lei Xu, Guangzhi Li, Wei Xu, Jennifer Rexford, “Optimizing Bulk Transfers with Software-Defined Optical WAN”, in ACM SIGCOMM, August 2016.

## Slide 56: Globally-distributed applications have big data to transfer over the WAN

## Slide 57: Software-Defined Networking (SDN)
Controller
Global traffic engineering with centralized control, e.g., Google B4, Microsoft SWAN
Given
Traffic Demand
Network Topology
Compute
Routing
Rate Allocation
Optimize
Completion Time
Deadlines Met
Network Topology

## Slide 58: Network-layer topology is built over an optical layer in a modern WAN
Network Layer
Optical Layer
Network
Link
Optical
Circuit
Seattle
Los Angels
Seattle
Los Angels
Network switch (Router)
Optical switch

## Slide 59: Reconfigure optical layer to change network-layer topology
R0
O0
R2
R3
R1
O1
O3
O2
Optical Layer
Router
Optical Switch
R0
R2
R3
R1
10
10
10
10
Network Layer
Configuration A
Optical Circuits

## Slide 60: Reconfigure optical layer to change network-layer topology
R0
O0
R2
R3
R1
O1
O3
O2
R0
R2
R3
R1
10
10
10
10
Network Layer
Optical Layer
Router
Optical Switch
Configuration A
R0
O0
R2
R3
R1
O1
O3
O2
R0
R2
R3
R1
10
10
10
10
Configuration B
Wavelength Multiplexing

## Slide 61: Reduce transfer completion time by topology reconfiguration
R0
R2
R3
R1
10
10
10
10
F0(Demand=10)
F1(Demand=10)
Plan A
F0
F1
Time
0.5
1
0
A
R0
R2
R3
R1
10
10
10
10
F0(Demand=10)
R0
R2
R3
R1
10
10
10
10
F1(Demand=10)
Plan B
Step 1
Step 2
F0
F1
Time
0.5
1
0
B
F0(Demand=10)
F1(Demand=10)
R0
R2
R3
R1
10
10
10
10
Plan C
F0
F1
Time
0.5
1
0
C
Unused
Capacity
Inefficiently Used
Capacity

## Slide 62: Owan: Joint control of optical and network layers to optimize data transfers
O0
O1
O2
Controller
Request Submission/
Rate Allocation
Routing
Configuration
Optical
Configuration
R0
R2
R1
C0
C1
C2
Access Network
Wide Area Network
Client DC
Router
Optical Switch

## Slide 63: Owan: Joint control of optical and network layers to optimize data transfers
Given
Traffic Demand
Network Topology
Compute
Routing
Rate Allocation
Optimize
Completion Time
Deadlines Met
Optical Topology
Constraints
# of Router Ports
Optical Reach
# of Regenerators
# of Wavelengths
Link Capacity

## Slide 64: Computing Network Configuration
Compute new topology based on traffic demand
  Use simulated annealing: probabilistically search for a topology with high throughput
Current
Topology
States: Different Topologies
Transition Probability
: throughput of current state
: throughput of neighbor state
: time-decaying parameter

## Slide 65: Computing Network Configuration
Generate neighbor state by random swapping links
  Heuristically search for optical circuits to build new links: balance the consumption of regenerators
E
A
D
B
C
E
A
D
B
C
Current state
(Current topology)
Neighbor state
(Neighbor topology)

## Slide 66: Computing Network Configuration
Compute throughput of neighbor state
  Routing: prioritize short paths
  Rate allocation: order transfers with classic scheduling disciplines for different objectives
Update network configuration
  Extend Dionysus to coordinate updates in optical and network layers
Average Transfer
Completion Time
SJF
(Shortest Job First)
EDF
(Earliest Deadline First)
……
# of Deadlines Met
Other Objective

## Slide 67: Implementation and evaluation
Implementation
  Software: Controller prototype
  Hardware: Testbed with 9 sites to emulate the Internet2 network
Evaluation
  Testbed experiments (9 sites)
  Simulations based on topologies and traces from an ISP network (~40 sites) and an inter-DC network (~25 sites)

## Slide 68: Evaluation: Improvement on transfer completion time

## Slide 69: Summary: Owan is a traffic management system for wide-area data transfers
1
Efficient algorithm
Dynamically reconfigure network topology
2
System prototype
Prototype on real testbed, evaluation on topology and traces from AT&T networks

## Slide 70: Research summary
Software-defined platforms for network management
  Dynamic service composition: CoVisor [NSDI’15]
  Dynamic update scheduling: Dionysus [SIGCOMM’14]
  Dynamic topology reconfiguration: Owan [SIGCOMM’16]
  Secure virtual switching on end hosts: DomS [Hot-ICE’12]
  Host-based network control: Sourcey [SOSR’16]
End-to-end network support for emerging applications
  Data center network: EnsembleRouting [INFOCOM’13]
  Cellular core network: SoftCell [CoNEXT’13]
  Mobile network: optimize video streaming [HotMobile’15]

## Slide 71: Thanks!
Xin Jin
xinjin@cs.princeton.edu
www.cs.princeton.edu/~xinjin